## Slide 1: Color Correction for Optical See-Through Displays Using Display Color Profiles
Srikanth Kirshnamachari Sridharan
Dr. Juan David Hincapié-Ramos
Dr. David R. Flatla (University of Dundee)
Dr. Pourang Irani
Notes: A very good afternoon.
My name is Srikanth Kirhsnamachari Sridharan,
I am a Masters student at Hci lab in university of Manitoba Canada.
I worked on this paper in collaboration with Dr. Juan David Hincapié-Ramos
Dr. David R. Flatla (University of Dundee)
Dr. Pourang Irani

## Slide 2: Introduction
Optical see-through displays (OSTD) allow users to view digital content and physical objects simultaneously. Additive OSTD have its own light source
Notes: Optical see-through displays allow users to view digital content and physical objects simultaneously
The most promising OSTDs are additive, they generate colors by creating light on their own in the different primary color (R,G,B).
Tranparent OLED diplays (on the left) or projector based HMDs (such as Google Glass) are commercially available examples of such additive display.

## Slide 3
Notes: However, additive OSTD s have a problem!
Display colors blend with the background.
This combination of colors causes the users’ perception of the color being displayed from what the color originally is!
Color are essential to clarity of the display, colors help humans to clearly understand the contents on the display.
Color blending negatively affects the usability of such displays as it impacts the legibility and color encodings of digital content.

## Slide 4
Gabbard et al. 2010. More than meets the eye: An engineering study to empirically examine the blending of real and virtual color spaces , VR 2010
Notes: Gabbard et al, in 2010, studied the different ways in which colors of a OSTD change with different backgrounds.

## Slide 5
Notes: This image shows color blending effort on the digital color yellow ,
(This Image will be changed to OLED)
Here is a OSTD displaying color yellow in 3 different background,
Black background- to the right in the color map you can see yellow being – yellow!
On red background- to the right in the color map you can see yellow being – moved towards red( shows orange)
Blue background-to the right in the color map you can see yellow being – moved towards green

## Slide 6
Kerr et al , Wearable mobile augmented reality: evaluating outdoor
user experience. VRCAI ’11
Usability Problem
Notes: This effect of color Blending has been studied before by various researchers mostly in the field of Augmented reality.
On usability issues and human perception
One such Eg is,
Kerr et al 2011, studies outdoor use of AR system, where they found on heavy influence from the background users used their hand on have a consistent bg to look at the contents !!
This shows that this influence of the background is a significant problem

## Slide 7
Content Based Solutions
Tanaka et al, An information layout method for an optical see-through head mounted display focusing on the view ability. ISMAR 08
Notes: There have been other solutions like ,
Tanaka et al. developed a layout system that relocates digital content to the darker areas of the display taking.
This methods might result in constant shift of the digital content for dynamic background.

## Slide 8: Hardware Based Solution
Kiyokawa et al, An Occlusion-Capable Optical See-through Head Mount Display
for Supporting Co-located Collaboration. ISMAR 2003
Notes: The main approach to occlusion has been to stop the light coming from the background by enhancing head-mounted displays with spatial light modulation (SLM) devices
Therefore, digital colors projected on the black areas are seen in their original hue and lightness. draw backs being the excess hardware and unavailability of the BG.
(clearly they were not going for style)

## Slide 9: Color Correction
Background
Alternate Color
?
Notes: Other solutions are called correction. Here the system finds an alternate color to show,
so that after blending with the background users perceive the color correctly.
For example…
This is a large research area within spatial augmented reality.

## Slide 10: Color Correction in OSTD
Weiland et al, Colorimetric and photometric compensation for optical see-through displays.
Notes: But in OSTD the only existing work on color corrections is by Weiland et al.’s.
They use foreground color as fed to the system and bg colors as captured
sRGB space was used for color calculations- in which colors accuracy cant be tested
They used Color Subtraction ( Show the second image’s empty spots)

## Slide 11
F(
Background
Digital Color
Bg Color
Blended Color
frender
fmaterial
Model – BP Method – Color Correction – Correction Analysis
Notes: Every display shows color a bit different , this is more pronounced in OSTD as each display has different display material, light source etc.
As you can see here the color blue shown is slightly changed when its shown on the display. In our model we account for this change render distortion function.
Similar the OSTD display material changes the color of the BG as it shown here with change in hue of bg color red . We count this by the material distortion function.
We argue in this work the color Belding is a mix of these distorted color than the original colors !!

## Slide 12
  Blended Color = frender(Digital Color) + fmaterial(Bg Color)
Model – BP Method – Color Correction – Correction Analysis
Notes: Out color beling modelios based on two functions, render DisTORtion and materail DisTORtion

## Slide 13
  Blended Color = frender(Digital Color) + fmaterial(Bg Color)
Model – BP Method – Color Correction – Correction Analysis
Direct Model – Weiland et al.
CAT – Bradford
CAT – Von Kries
CAT – Scaling
Bin Profiles
{
Notes: There are different wasys in which frendercan be sloved such as
Dm cat , we prent to you a new method called Bp method,
And vaLIDATE IT AGAINST THE OTHER METHODS

## Slide 14
Model – BP Method – Color Correction – Correction Analysis
  frender() = Direct Method ( )
  return ;
Notes: WHEN USING DIRECT METHOD,
WHEN fg color is fed to the system, the Dm retuts the same fg to be used , this is synonymous to ro Wiland et al work

## Slide 15
Model – BP Method – Color Correction – Correction Analysis
  frender() = CAT-Von Kries ( )
  * 
  return ;
Notes: CAT are established methods to estimate the colors a display can render based on the brightest white it can emit.
They are based on matirx trasformations
When a system feeds fg color to CAT , the cat transforms the color using a std matrix and returns the transformed color

## Slide 16
  frender() = Bin Profile method ( )
  return ;
  Display Profile[ ] 
Model – BP Method – Color Correction – Correction Analysis
Notes: Now we prest to you a new method , BP which is uses the display profile of a given display ,
When a fg is given to BPO mehod ,
Exact value of how this fg is shown by the display is returned!!
This BP we bilive forms a core part of out contibution ,
Now I will explain how to create a BP
Divides sRGB color space (over 16 million colors) into a smaller set of 8376 perceptually different bins.
We translated the sRGB gamut into the CIE LAB color space and divided it into bins of 5X5X5
This approach guaranties all colors inside a bin are within one Just Noticeable Difference (1 JND ~ 2.3 in Euclidean distance)
we measured how each bin is rendered by each of our three displays on a black background which is shown here for all 3 displays
P37-hundred had a wide color space and close to sRGB when compared to p2200 and TOLED
Create a look up table which is Binned Profile

## Slide 17
Model – BP Method – Color Correction – Correction Analysis
Notes: We know rgb colors anount to 16 million continues color space

## Slide 18
Model – BP Method – Color Correction – Correction Analysis
Heer et al, Color naming models for color selection, image editing and palette design.
CHI ’12.
Notes: We divide this color space into finte numbre of 8376 colors , we do this by binning them to one represeationve color for ever 5X5X5 bins in LAB space
This approach guaranties all colors inside a bin are within one Just Noticeable Difference (1 JND ~ 2.3 in Euclidean distance)

## Slide 19
Notes: Then we displayed these colors on two projection based ostd & 1 toled and measured it using a colorimeter

## Slide 20
Model – BP Method – Color Correction – Correction Analysis
Notes: On measuring the one of the projection based display gave a display profile which looks almost similar to srgb

## Slide 21
Model – BP Method – Color Correction – Correction Analysis
Notes: While Toled gave a display profile which look some what reduced

## Slide 22
Model – BP Method – Color Correction – Correction Analysis
Notes: We now had a one to one mappingbetween acolor and how its shown on a display

## Slide 23
Model – BP Method – Color Correction – Correction Analysis
Notes: Forr example a color blue which is

## Slide 24
  Blended Color = frender(Digital Color) + fmaterial(Bg Color)
Direct Model – Weiland et al.
CAT – Bradford
CAT – Von Kies
CAT – Scaling
Bin Profiles
{
Model – BP Method – Color Correction – Correction Analysis
Notes: Till now I have shown you various method to account for frender function , we handedled fmaterial through caputing the bg through the screen using a colorimtere
Validation the accuracy of the different frender functions by measuring how accurately they predict color blending

## Slide 25: Prediction Error
Background
Prediction
Measured
Distance in LAB = Error
Model – BP Method – Color Correction – Correction Analysis
Notes: We used 838 fg colors on each of our 23 bg colors, measured the blend.
We find the error in our prediction by finding Euclidean distance in lab space between the predicted value and the measured blend

## Slide 26
Results Visualization
Prediction Error – Distance in LAB
Bg colors used
Model – BP Method – Color Correction – Correction Analysis
Notes: This visualization shows prediction error value
across 23 bg macbeth chart colors for bg whhich is shown in x axis
And eq distance in y
First 2 boxes shows: there is a large spread in error for those backgrounds
Box3: shows that for this particular bg , the prediction error was low ,
Ideally this is how all bg should look for a low error rates
Box4: shows the error spread is concentrated between 10 – 40
the hue of blue indicates more value fell in that region .
Error rate at the bottom near 0, represent prediction with low error rate

## Slide 27
Model – BP Method – Color Correction – Correction Analysis
Notes: This visualization was used to compare the 5 models we had, over 3 displays in 2 different bg config
Bp In all cases was found to be the most accurate in predicting the blend
This validates the use of BP to predict how colors blend

## Slide 28: Color Correction
Background
?
?
BP Correction Algorithm
Digital
Color
Target Color
Model – BP Method – Color Correction – Correction Analysis
Notes: When color yellow is shown in red bg , it moves towards orange ,
Color correction needs to find a alternate color which on blending with bg will give yellow
We use BP correction algorithm to pick this alternate error

## Slide 29
procedure BP-PRESERVATION (Display,Foreground,
Background)
BinF oreground = findBin(Foreground)
DispF oreground = lookup(Display;BinF oreground)
Error = INFINITY
for each Color in Display
Prediction = addXY Z(Color;Background)
TmpError=distance(Prediction,DispForeground)
if TmpError<Error
Error = TmpError
ColorToShow = Color
CorrectedColor=revLookup(Display,ColorToShow)
end for
returnCorrectedColor
end procedure
Model – BP Method – Color Correction – Correction Analysis

## Slide 30
Target =
… 8376 times
Color to Show =
Model – BP Method – Color Correction – Correction Analysis

## Slide 31: BP Color Correction
Background
?
?
BP Correction Algorithm
Digital
Color
Target Color
Measured
Distance in LAB = Error
Model – BP Method – Color Correction – Correction Analysis
Notes: This color is then applied on the screen
Which happens to be green
The correction error is calculated by finding the distance between the color we desire and the actual blend after correction

## Slide 32: Quantitative Analysis
Kruskal-Wallis test was done, Sig <0.001
Model – BP Method – Color Correction – Correction Analysis
Notes: We generally found neutrals to have low error rate, other than that we found light colors in cyan blue region preforming consistently better among all the other color regions across the bg.
All colors in light region performed better on dark bg
Dark colors in high intensity bg performed the worst !!

## Slide 33: Design Implications
Use light neutral colors for information that needs to be preserved best
If more hue is needed, designers can use light colors in the Cyan-Blue region
Dark colors should be avoided for text and color-encoded information
Usage of color themes based on the background will be wise
Model – BP Method – Color Correction – Correction Analysis
Notes: A UI designer for OSTD show keep following points in mind
Use Light neutral colors for information that needs to be preserved best (text , icons etc)
If more hue is needed, designers can use light colors in the Cyan-Blue region (alerts)
Dark colors should be avoided for text and color-encoded information
Usage of color themes based on the background will be wise
Have in mind there we are not recommending these to preserve contrast we are more concern about color

## Slide 34: Contributions
A color blending model for OSTD
Display Binned Profile (BP) – main factor
BP-based color correction
Correction analysis of various digital colors
Notes: So what is our contributing visa this work ?
A present a new Color blending Model for OSTD
Binned Profile (BP) – To handle Render Distortion
BP Based Color Correction
Design guidelines for OSTD

## Slide 35: Future Work
Notes: We are currently working on a algorithm which is not brute force.
Also working to implement this on a HMD

## Slide 36: Acknowledgements
Dr. Juan David Hincapié-Ramos
Dr. Pourang Irani
Dr. David R. Flatla
Special thanks to Jango Guo
NSERC for funding and people at HCI lab In university of Manitoba

## Slide 37: Thank you, Questions?
Presented by,
Srikanth Kirshnamachari Sridharan

## Slide 38: Result
Model/BP Method/Color Correction/Correction Analysis
Notes: We created correction heat maps for all 3 displays,
The heat map shows generally colors for p22-hundered and TOLED were better corrected than the p3700
This is due the both these displays have limited color profile, so the distqance between a color to shown in bin and how it measured fg will always be small.
We also found a trend in fg color always got corrected better for low intensity bg , with the correction error increasing with the intensity of the bg.
We took the p3700 and studied it further has it had wider range colors , which are typlically needed for rich multimedia contests

## Slide 39: Quantitative analysis
Kruskal-Wallis test was done, Sig <0.001
Notes: We decided to do quantitative analysis for bp and direct model.
Here green bars rep bg in plain config, blue bars rep bg in adjusted config
Graph shown there is a fall in green pars perdition error between bp and direct model for all 3 displays.
This shows accounting for render distortion with the help of bp decreases the prediction error.
While both the distortions were accounted for the prediction accuracy increased as shown in the graph comparison between plain and adjusted config using bp on all 3 displays.
However addressing only the material distortion , does little change to the error rate
this result shows the render distortion constitutes the core of color blening in OSTD

## Slide 40: Just Noticeable Difference
Notes: JND is the Euclidian distance between 2 given color in a color space with in which the colors appear same to humans.
In XYZ space it varies with each color, but in uniform spaces like LAB and LUV its constant number ( 2.5 in lab).

## Slide 41: Setup
Notes: Image on the left shows how the set up was for both projection based and TOLED
Image on the right © shows how the actual setup was.
And image d shows the out light controlled environment
We used cs200 colorimeter to measure the color values.

## Slide 42
Notes: Cat fg colors

## Slide 43: Result
Notes: Prediction result viz

## Slide 44: Direct Method prediction
Background
?
?
Digital Color
Prediction
Bg Color
Digital Color
Model/BP Method/Color Correction/Correction Analysis
Notes: Direct Method:
Synonymous to Weiland et al work
The digital color is simply added to the background
It ignores both render and material distortion

## Slide 45: CAT Method prediction
Background
?
?
Digital Color
Prediction
Bg Color
CAT
Transformation
Model/BP Method/Color Correction/Correction Analysis
Notes: CAT
CAT are established methods to estimate the colors a display can render based on the brightest white it can emit. They are based on matirc converstions
In other words we hoped that they could potentially handle render distortion